## Slide 1
Shell and Tube Heat Exchanger
Presented by : Usman Akram, Jeremy Baker, Jonathan Ferguson and Daniel Sigala
Photo by https://www.dhtnet.com/products/shell-tube-heat-exchangers/

## Slide 2
Overview of Experiment
In this experiment, a shell and tube heat exchanger is modeled and simulated to find the heat transfer rate of the heat exchanger and its efficiency..
We designed a heat exchanger using solidworks. A fluid simulation was done to see how the heat exchanger performed under ideal conditions..
The shell and tube design had an efficiency of .37 with a overall heat transfer of Qactual =2.32 kW and theoretical heat transfer of Qtheoretical= 6.27 kW.
Some of the parameters we modified was the mass flow rate of the fluids and surface area of the pipes to achieve maximum heat transfer rate.

## Slide 3
What is a Shell and Tube Heat Exchanger?
A Shell and Tube heat exchanger is a simple system that transfers heat by running cool and hot fluids in a series of pipes.
The shell is the outer portion of the system which is a large pressure vessel with a bundle of tubes running on the inside of the shell. Baffles are used to control the flow of the fluid inside the shell.
Heat is transferred using conduction through the bundle of pipes inside the shell and convection of the fluids.
Most commonly used in oil refineries and large chemical processes because of its high pressure applications.
Cross section of shell and tube model using Solidworks.

## Slide 4
How does a Shell and Tube Heat Exchanger Work?
This model has crossflow which means the fluid in the tube bundle flows in the opposite direction from the fluid in the shell.
The baffles direct the fluid in the shell across the tube bundles in a zigzag formation increasing turbulent flow for more cross-flow and mixing inside the shell.
This is a single pass model which means the fluid in the tube bundle passes through the shell horizontally one time.
Conduction transfers energy through the walls of the pipe so the fluids do no mix.
Convection transfers energy throughout the fluid inside the system that the fluid is in.
Vector model of flow direction.

## Slide 5
View of Shell and Tube Heat Exchanger
Isometric view of tube bundle and baffles.
Shell and Tube break down.

## Slide 6
Simulation of Heat Transfer in System

## Slide 7
What Results did the Shell and Tube Produce?
The overall heat transfer for the heat exchanger was found to be Qactual =2.32 kW. The theoretical heat transfer was Qtheoretical= 6.27 kW giving us an effectiveness of .37.
Initial conditions: Cold Inlet = 20°C
Hot inlet = 50°C
From the heat transfer the temperature exchange provided us with final values of the TCO being 31.12°C and the THO being 38.93°C
Temperature distribution of the fluids across the heat exchanger.

## Slide 8
What do these Results Mean?
Temperature change over time.
The temperature of the fluid drops as it travels through the tube exit.
Counter-flow allows for the most heat transfer to occur because the cold fluid flows across the hot fluid inlet.

## Slide 9
Conclusion
Solidworks is a great tool when running 3D visual simulation.
Solidworks is also a great tool when running programs numerically.
Shell and tube heat transfer has an overall equal temperature distribution.
Through trial and error we were able to get an efficiency of 37%.
With a simulation there will not be any uncertainty.
List of applications: HVAC, Refrigeration, and compressors.

## Slide 10
Video Presentation

## Slide 11
Any Questions?